## Slide 1: Kirchhoff-Love Shells with Arbitrary Hyperelastic Materials Jiahao Wen, University of Southern California Jernej Barbič, University of Southern California

## Slide 2: Thin shells
Architecture (roof)
Parachutes
Biological membranes (fascia)
Paper [Grinspun et al. 2003]
Cloth [Narain et al. 2012]
Metal sheets

## Slide 3: Hyperelastic volumetric materials
ARAP
[Sorkine et al. 2007]
Stable Neo-Hookean
[Smith et al. 2018]
Symmetric Dirichlet
[Smith et al. 2019]
Symmetric ARAP
[Smith et al. 2019]
STVK
[Barbič et al. 2012]

## Slide 4
Problem
Thin shell simulation
Volumetric simulation
A thin shell is simply a very thin volumetric object.
The thickness is close to 0, but not 0!
Can we use 3D solid mechanics and volumetric hyperelastic materials to simulate thin shells? 🤔

## Slide 5
We expand the volumetric elastic energy to a Taylor series in the thickness .
We contribute such a method…
Our formulation works for arbitrary hyperelastic materials, arbitrary thin-shell rest shapes, and arbitrarily large deformations.
Notes: Our paper contributes such a method.
We expand the volumetric elastic energy to a Taylor series in the thickness ℎ. When the thickness is small, we can reduce 3D elasticity onto the 2D manifold.
We also prove that our formulation…

## Slide 6
Better convergence to analytical result
Why not simulate a volumetric thin shell directly using a volumetric mesh?🤔
Tet mesh
Triangle mesh
extrude up and down
Ours
Tet mesh

## Slide 7
Visual comparison to volumetric simulation

## Slide 8
We can simply “plug in” any volumetric hyperelastic materials and simulate “Co-rotational cloth”, “ARAP cloth”, etc.
Benefits

## Slide 9
We can simply “plug in” any volumetric hyperelastic materials and simulate “Co-rotational cloth”, “ARAP cloth”, etc.
Benefits

## Slide 10: SPD projection
Many simulation techniques have been designed to benefit volumetric simulation.
They can now be applied to thin shells.

## Slide 11
Related work
[Cirak et al. 2001]
[Clyde et al. 2017]
[Chen et al. 2018]
[Lin et al. 2022]

## Slide 12
Normal to mid-surface remains normal to mid-surface after deformation.
The thickness does not change during deformation.
The thickness is small relative to object size and curvature radius.
Commonly used
Simplify problem
Kirchhoff-Love thin-shell assumption
[image source: Wikipedia]
rest shape
deformed shape
mid-surface
normal

## Slide 13
Parameterization
13

## Slide 14
: defined in our paper
Applying Neumann series:
: defined in our paper
for stretching
Bending happens because of non-zero thickness.
3D Solid Deformation gradient
for bending
Difficult to compute for integration!

## Slide 15
Intuitive explanation for bending
🪄
Transverse view
[Tamstorf et al. 2013]

## Slide 16
Elastic energy density
: the First Piola-Kirchhoff stress tensor
, , : defined in the paper

## Slide 17
Elastic energy
Integration:
: the First Piola-Kirchhoff stress tensor : rest Gauss curvature
, , : defined in the paper
■: stretching
■: bending

## Slide 18
Generalization of [Chen et al. 2018]
Missing terms!
Missing terms!
Under the small in-plane stretch assumption in [Chen et al. 2018]

## Slide 19
Solution: eliminate using finite differencing
Problem: should not appear in energy
Still , but no !!
This would make calculation of forces and stiffness matrices impractical. ☹️

## Slide 20
F-Based energy vs. E-Based energy
Deformation gradient:
Green strain tensor:
equivalent
More commonly
used in practice!
Our method can handle both F-based and E-based energies!
Our method benefits from existing F-based stability analyses.

## Slide 21
Categorization of KL-shell energies
……
……
Volumetric materials
Thin-shell materials
❓
Q: For KL thin-shells, is it possible that two hyperelastic volumetric energies result in identical thin-shell energies?🤨

## Slide 22
Categorization of KL-shell energies
Q: For KL thin-shells, is it possible that two hyperelastic volumetric energies result in identical thin-shell energies?🤨
A: and produce identical thin-shell energies iff they agree on each deformation gradient of the specific form
: arbitrary rotation matrix.
(see detailed proof in our paper 🤓)

## Slide 23
Isotropic KL materials
Categorization of KL-shell energies
For isotropic materials
Symmetric energies of two principal stretches

## Slide 24
Material design
The user can design KL thin-shell materials through symmetric functions
But the design is still tedious because the space of symmetric functions is large! 🤯
2D Valanis-Landel hypothesis

## Slide 25
3-parameter Valanis-Landel family
Simplest that permit controlling small strain and large strain behavior!
: scalar parameters tuned by users
Small deformation, same behavior.
Large deformation, higher has larger stiffness.

## Slide 26
Suspension under different gravity and nonlinearity
Neutral shape
Low
High
gravity
gravity
controls nonlinearity!

## Slide 27: Material Design
Low nonlinearity
High nonlinearity

## Slide 28: Discretization
Discrete Fundamental Forms [Weischedel 2012]
Mean curvature:
Gauss curvature:
Canonical triangle
Deformed triangle
See implementation details in our paper.

## Slide 29: Anisotropic materials
Anisotropic ARAP; a is the anisotropic direction

## Slide 30: Different materials

## Slide 31: Different materials

## Slide 32: Control bendability by changing thickness
Large thickness
Small thickness

## Slide 33: Control bendability by changing thickness
Large thickness
Small thickness

## Slide 34: Thanks!
No animals were harmed during the simulation 